## Slide 1: Networking Jump Start
If you can do this, you can do anything.

## Slide 2: IP ADDRESSING
The name of a computer, printer, router, switch, X-Box, etc. on a network is an IP Address.
In general, IP Addresses should represent only one computer in the world (they are unique).
The front of the IP Address identifies the business where the computer is located, and the back identifies the specific computer in that business.
There are two IP Addressing systems, IPv4 and IPv6, but we will be focusing on IPv4, as that is the best place to start.

## Slide 3: IPv4 Addressing
192.168.10.22
The red numbers are the “name of the business.”
The blue number is “the specific computer.”

## Slide 4: Windows Wants More Numbers!

## Slide 5: We Need Three Different Numbers
192.168.10.22 – IP Address
255.255.255.0 – Subnet Mask
192.168.10.1 – Default Gateway

## Slide 6: We Need Three Different Numbers
192.168.10.22 – IP Address (Our Computer)
255.255.255.0 – Subnet Mask (Business Size)
192.168.10.1 – Default Gateway (Router)

## Slide 7
INTERNET

## Slide 8
INTERNET
IP: 192.168.10.22
SM: 255.255.255.0
DG: 192.168.10.1

## Slide 9
INTERNET
IP: 192.168.10.22
SM: 255.255.255.0
DG: 192.168.10.1
?

## Slide 10
INTERNET
IP: 192.168.10.22
SM: 255.255.255.0
DG: 192.168.10.1
IP: 192.168.10.23 through
192.168.10.254

## Slide 11
INTERNET
IP: 192.168.10.22
SM: 255.255.255.0
DG: 192.168.10.1
IP: 192.168.10.23
SM: 255.255.255.0
DG: 192.168.10.1

## Slide 12
INTERNET
IP: 192.168.10.22
SM: 255.255.255.0
DG: 192.168.10.1
IP: 192.168.10.23
SM: 255.255.255.0
DG: 192.168.10.1
IP: 192.168.10.1
SM: 255.255.255.0

## Slide 13
INTERNET
IP: 192.168.10.22
SM: 255.255.255.0
DG: 192.168.10.1
IP: 192.168.10.23
SM: 255.255.255.0
DG: 192.168.10.1
IP: 192.168.10.1
SM: 255.255.255.0
I am the Default Gateway!

## Slide 14: Cables!
The two main cables are copper (Cat5, Ethernet) and fiber optic.
Copper is cheap and works well enough.
Fiber is expensive and, well, expensive.

## Slide 15: Equipment
NIC – Network Interface Card – Provides a way for your laptop, desktop, phone, printer, etc. to connect to the local network.
Switch – Connects multiple devices together to form the local network.
Router – Connects networks together, such as your local network to the Internet.
Firewall – Can look at traffic and say “no” to passing things along.
WAP – Shares a single switch port with multiple wireless devices.

## Slide 16: Network Interface Card

## Slide 17: Switch

## Slide 18: Router

## Slide 19: Firewall

## Slide 20: Wireless Access Point

## Slide 21: PoE Injector

## Slide 22: Let’s Build a Network